## Slide 1
ASSEMBLER DIRECTIVES

## Slide 2
What is Assembly language?
It is a low-level languages for programming computers , microprocessors, microcontrollers and other IC .
Assembly Language programs are composed of two types.
Instructions
Directives (Pseudo Instructions)
What is Assembler Directive?
It is a statement to give direction to the assembler to perform task of the assembly process.

## Slide 3: Categories of Assembler directives
Based on the functions performed by the assembler directives they are classified as,
Data Definition and Storage Allocation Directives
Program Organization Directives
Alignment Directives
Programs End Directives
Value Returning Attribute Directives
Procedure Definition Directives
Macro Definition Directives
Data Control Directives
Branch Displacement Directives
Header File Inclusion Directives
Target Machine Code Generation Control Directives

## Slide 4
SYMBOLS:
It is used to signify different components of the ALP (assembly Language Program).
Symbols consist of following characters.
  Upper case & lower case alphabets: A to Z; a to z
  Digits: 0 to 9
  Special characters: $, ?, @, _ (underscore)
  No distinction between an uppercase and lowercase letter
  A hexadecimal no. starting with A to F must begin with “0” (zero) ; otherwise will be taken as a symbol

## Slide 5
VARIABLE
Variables are the symbols whose values can be dynamically varied during run – time (running program).
Rules for Variable Names.
A variable can have any one of the following characters.
A to Z; a to z; 0 to 9; @; _ (underscore).
A Variable name must start with letter or Underscore.
Length of the variable name depends on the assembler, normally max. length is 32 characters.
There is no distinction between the uppercase and lower case letters.
Examples:
Valid : Num1, NUM, _data, Total_marks
Invalid: 1num1 , $ , $num

## Slide 6
CONSTANTS:
These are symbols whose values can not be varies while running a program.
A numeric constant may be a binary, decimal or hexadecimal number.
Symbols B, D & H must be used at the end of a binary, decimal and hexadecimal number, respectively.
Suppose the number does not end with any of the following then it will be treated as Decimal number.
Binary constant can have only 0 or 1(BITS).
Decimal constant can have only 0 -9.
Hexadecimal numbers have both 0-9 and characters (A-F).
Examples:
Valid : 1010, 1010D, 10101H, 0F1H, 1010B
Invalid : 1021B, 0F1,10DD

## Slide 7: DATA DEFINITION AND STORAGE ALLOCATION DIRECTIVES
Data declaration directives: DB, DW, DD, DQ, DT, STRUCT and RECORD.
DB - The DB directive is used to define byte type variable.
The range lies between 0 -255 for unsigned numbers and -128 to 127 for signed numbers.
GENERAL FORM
nameOfVariable DB InitializationValue(,s)
Examples:
TOTAL DB 0
DATA DB A
MSG DB ‘Hello World’
Num DB 100 DUP(?)

## Slide 8
2. DW
The DW directive is used to define a WORD type(2 byte) variable.
The range lies between 0 -65535 for unsigned numbers and -32768 to +32768 for signed numbers.
GENERAL FORM
nameOfVariable DW InitializationValue(,s)
Examples:
TOTAL DW 0
DATA DW ?
MSG DW ‘Hello World’
Num DW 100 DUP(?)

## Slide 9
DD (DEFINE DOUBLE WORD)
The DD directive is used to define a DOUBLE WORD type(4 byte) variable.
The range lies between 0 to 232-1 for unsigned numbers and - 232-1 to
+ 232-1 -1for signed numbers.
GENERAL FORM
nameOfVariable DD InitializationValue(,s)
Examples:
TOTAL DD 0
DATA DD ?
MSG DD ‘Hello World’
Num DD 100 DUP(?)

## Slide 10
DQ (DEFINE QUAD WORD)
The DQ directive is used to define a QUAD WORD type(8 byte) variable.
The range lies between 0 to 264-1 for unsigned numbers and - 264-1 to
+ 264-1 -1for signed numbers.
GENERAL FORM
nameOfVariable DQ InitializationValue(,s)
Examples:
TOTAL DQ 0
DATA DQ ?
MSG DQ ‘Hello World’
Num DQ 100 DUP(?)

## Slide 11
6. DT (DEFINE TEN BYTES)
The DT directive is used to define a TEN BYTES type(8 byte) variable.
The range lies between 0 to 280-1 for unsigned numbers and - 280-1 to
+ 280-1 -1for signed numbers.
GENERAL FORM
nameOfVariable DT InitializationValue(,s)
Examples:
TOTAL DT 0
DATA DT ?
MSG DT ‘Hello World’
Num DT 100 DUP(?)

## Slide 12
7. STRUCT : Structure Declaration
The directive STRUCT is used to declare a datatype which is a collection of primary data types(DB,DW,DD).
GENERAL FORM
StructureName STRUCT
…..
;
structureName ENDS
Example:
STUDENT STRUCT
rollno dw ?
name db 10 dup(?)
STUDENT ENDS

## Slide 13: 8. RECORD
The directive RECORD is used to define a bit pattern within a byte or word.
GENERAL FORM
RecordName RECORD FieldSpecification1….. FieldSpecificationN
Examples:
Bits 7, 6, 5 : Baud Rate
Bits 4, 3 : parity
Bits 2 : Stop bits
Bits 1, 0 :Word Length
Data RECORD BAUD : 3, PARITY :2 , WORDLENGTH: 2

## Slide 14: PROGRAM ORGANIZATION DIRECTIVES
Program Organization Directives : SEGMENT, ENDS, ASSUME, GROUP
SEGMENT
SEGMENT directive is used to indicate the start of a logical segment.
Syntax:
Segment_name SEGMENT [byte/word]
Examples:
_Data Segment
…….
_Data Ends

## Slide 15
2. ENDS - End Segment
ENDS - indicates the end of a logical segment.
Syntax:
Segment_name ENDS
Examples:
_Code Segment
………
_Code Ends

## Slide 16
ASSUME Directive
The ASSUME directive is used to tell the assembler that the name of the logical segment should be used for a specified segment.
GENERAL FORM
ASSUME SegReg : SegName. ……SegReg : SegName
Example:
ASSUME CS:CODE ;
ASSUME DS:DATA ; ASSUME DS:DATA ; CS : CODE, SS :STACK, ES ; EXTRA

## Slide 17
4. GROUP
It used to group the logical segments named after the directive into one logical group segment.
The grouped segment will have the same segment base.
GENERAL FORM
GroupName GROUP : SegmentName1,………SegmentNameN
Examples:
SmallModel GROUP Data, Code, Stack, Extra

## Slide 18: Alignment directives
1. EVEN
It instructs the assembler to increment the location of the counter to the next even address .
If the location counter is already pointing to even memory address, it should not be incremented.
GENERAL FORM
EVEN
Examples:
_Data Segment _data Segment
A DB 10 A DB 10
B DW 100 dup(?) EVEN
_Data Ends B DW 100 dup(?)
_Data ENDs

## Slide 19: 2. ORG (ORIGIN)
ORG assigns the location counter with the value specified in directives.
It helps in placing the machine code in the specified location while translating the instruction into machine code by the assembler.
GENERAL FORM
ORG [$+] NumericValue
Example:
ORG 2000H
The statement ORG 2000H tells the assembler to set the location counter to 2000H.
ORG $ + 10
ORG $

## Slide 20: Programs End directives
The program end directive is used to inform the assembler the physical end of the program.
GENERAL FORM
1. END
2. END LABEL
Examples:
Main proc
…..
Main Endp

## Slide 21: Value returning Attribute directives
Value returning Attribute directives are LENGTH, SIZE, OFFSET and TYPE.
LENGTH
  It informs the assembler about the number of elements in a data item such as an array.
  If array is defined with DB, then it returns the number of bytes allocated to a variable.
  GENERAL FORM
  LENGTH VariableName
  Examples:
  _data Segment
  Name db 100 dup(?)
  B DW 50dup(?)
  _data End
  MOV AX, LENGTH Name ; AX = 100 (byte array size)
  MOV BX , Length B : BX = 50

## Slide 22
SIZE
  It is same as the LENGTH directive except that it returns the number of bytes allocated to the data item instead of number of elements in it.
  GENERAL FORM
  SIZE VariableName
  Examples:
  _data Segment
  Name db 100 dup(?)
  _data End
  MOV AX, SIZE NAME ; AX = 100 number of bytes allocated to name

## Slide 23
OFFSET
The directive OFFSET informs the assembler to determine the displacement of the specified variable with respect to the base of the segment.
It is usually used to load the offset of a variable into the register. Using this offset value, a variable can be referenced using indexed addressing modes.
GENARAL FORM
OFFSET VariableName
Example:
  _data Segment
  Name db ‘Hello world’
  A dw 50 dup (?)
  _data End
  MOV DX, OFFSET Name
  MOV SI, OFFSET A
  MOV AX , [SI]

## Slide 24: 4. SEG: Segment
The directive SEG is used to determine the segment in which the specified data item is defined.
GENERAL FORM
SEG VariableName
Example:
  _data Segment
  Name db ‘Hello world’
  A dw 50 dup (?)
  _data End
  MOV DX, SEG Name
  MOV SI, SEG A

## Slide 25: 5. TYPE:
The directive TYPE is used to determine the type of the data item. It determines the number of bytes allocated to the data type. Assembler allocates one byte to DB, two bytes to DW, and four bytes to DD type variable definition.
GENERAL FORM
TYPE VariableName
Example:
  _data Segment
  CHAR db ‘Hello world’
  AMOUNT dw 50 dup (?)
  _data End
  ADD BX , TYPE CHAR ; BXBX+1
  ADD BX , TYPE AMOUNT ; BXBX+4

## Slide 26: Procedure Definition directives
Procedure definition directives used to define subroutines. Like PROC and ENDP.
PROC : PROCEDURE
The directive PROC indicates the beginning of a procedure. The directive PROC follows the name of a procedure. The term NEAR or FAR follows the PROC indicating the type of a procedure. If this term is discarded, then the assembler assumes NEAR as the type specifier. The directive PROC is used with the directive ENDP to enclose the procedure code.
GENERAL FORM
ProcedureName PROC [NEAR/FAR]
Example:
  HEXA PROC NEAR
  FACT PROC FAR

## Slide 27: ENDP: End of Procedure
The directive ENDP informs the assembler the end of a procedure. The directives ENDP and PROC must enclose the procedure code.
GENERAL FORM
ProcedureName ENDP
Example:
  HEXA PROC NEAR
  …
  HEXA ENDP
  FACT PROC FAR
  ……
  FACT ENDP

## Slide 28: Macro Definition directives
The Macro definition directives are used to define macro constants and macro functions. The directives EQU, MACRO, and ENDM are used in the definition of a macro.
EQU : Equate Macro Constant
The directive EQU is used to declare the symbols to which some constant value is assigned. Such symbols are called as macro symbols. Macro Assembler will replace every occurrence of the symbol in a program by its value.
GENERAL FORM
SymbolName EQU expression
Example:
  1. NUM EQU 100
  2. INCREMENT EQU INC

## Slide 29: 2. MACRO
The directive MACRO informs the assembler the beginning of a macro. It consists of the name of a macro followed by the keyword MACRO and macro arguments if any.
The directives MACRO and ENDM must enclose the definition(s), declaration(s), or a small part of the code which have to be substituted at the invocation of a macro.
GENERAL FORM
MacroName MACRO [ Argument1,……..ArgumentN ]
Example:
  PRINTSTRING MACRO MSG
  MOV AH , 09
  MOV DX , OFFSET MSG
  INT 21H
  END
  Code segment
  printstring msg
  Code Ends

## Slide 30: 3. ENDM: End of Macro
The directive ENDM informs the assembler the end of the macro. The directives MACRO and ENDM must enclose the definition(s), declaration(s), or a small part of the code which have to substituted at the invocation of a macro.
GENERAL FORM
ENDM
Example:
  PRINTSTRING MACRO MSG
  MOV AH , 09
  MOV DX , OFFSET MSG
  INT 21H
  END

## Slide 31: Data Control directives
It used to declare the variables used in communication of information between the program modules.
The data control directives are PUBLIC, EXTRN, and PTR.
1. PUBLIC:
It informs the assembler that the specified variable or segment can be accessed from other program modules.
It helps in managing the multiple program modules by sharing the global variables or procedures.
GENERAL FORM
PUBLIC Variable1, ………VariableN
Example:
  PUBLIC XMAX, YMAX _data Segment
  xmax dw 640
  ymax dw 350
  public xmax, ymax
  _data ends

## Slide 32: 2. EXTRN: External
The directive EXTRN informs the assembler that the data items or label following the directive will be used in a program module which is defined in other program modules.
GENERAL FORM
EXTERN Variable1 : ReferenceType1, ………VariableN : ReferenceTypeN
Example:
  EXTERN XMAX, YMAX : WORD
  _data segment _data Segment
  Xmax dw 640 ….
  Ymax dw 350 extrn xmax , ymax : word
  _data Ends _data ends

## Slide 33: 3. PTR: Pointer
The directive PTR is used to indicate the type of memory access (BYTE/WORD/DWORD).
For instance, if the assembler encounters the instruction like INC [SI], it will not be able to decide whether to code for byte increment or word increment.
It can be resolved by using PTR directive with the instruction as INC BYTE PTR [SI) for byte increment or INC WORD PTR [SI) for word increment. The directive PTR can also be used to override the type declaration of a variable, i.e., if a variable is declared as word, it can be accessed as byte.
Example:
  INC BYTE [DI]
  INC WORD [DI]

## Slide 34: Branch Displacement Directives
The Branch displacement directives are used to control the branch displacement. The branch displacement directives are SHORT and LABEL.
1. SHORT:
The directive SHORT informs the assembler that one byte displacement is required to code a jump instruction.
The target address must be in the range of -128 bytes to +127 bytes from the address of jump instruction.
Example:
  …….
  JMP SHORT SKIP JMP SHORT SKIP
  ………
  SKIP :

## Slide 35: 2. LABEL
The directive LABEL assigns a name to the current value in the location counter.
The label directive must be followed by the definition of data type to which label is associated.
GENERAL FORM
LABEL labelName LabelType
Examples:
Stack Segment
data dw 100dup(?)
stacktop Label word
stack Ends

## Slide 36: Header File Inclusion directives
The Header File Inclusion directive is used to define a include file header. The header file inclusion directive is INCLUDE.
INCLUDE
The directive INCLUDE informs the assembler to include the statements defined in the include file.
It is useful to place all the data and frequently used macros into a file known as include file or header file.

## Slide 37
GENERAL FORM
INCLUDE < file path specification >
Examples:
INCLUDE MACRO. LIB
INCLUDE C:\MULIB\CONST.H

## Slide 38: Target Machine Code Generation
The assembler will recognize only 8086 instructions by default. It is because the program that confirm themselves to the 8086 instruction set can run on any IBM PC, irrespective of the microprocessor (8086, 80186, ..) used.

## Slide 39
Thank you